2015-01-30

Commands for CXN50 Solid

Two wire TTL-RS232 Bus with echo: 19200 Baud,No Parity,1 Stopbit,8 Data

Each character is echoed by the CXN50
Each Byte is an ASCII character.
Wrong characters are echoed followed by a ?
PC is only allowed to send after receiving echos.
Single Byte commands

Command	Item	Answer of CXN50
0x0D = CR	1	0 = Initializing not finished / 1 = Initializing finished;
0x20 = Blank	1 / 2 / 3 / 4 / 5 / 6 / 7 / 8 / 9 / 10 / 11 / 12 / 13 / 14 / 15 / 16 / 17 / 18 / 19	Blank: CXN50 sends / Items separated by ';' / Load current in digits; / Load current;(resolution 10mA) / Charge current in digits; / Charge current;(resolution 10mA) / Internal Temperature in digits;; / Battery Voltage in digits(with current); / Firmware version; / Load state; / inverter state: / Charge state; / Boostcharge activ :1; / Equalcharge activ :2 / Gel :4; / Night :8; / External Tempearture error: 16 / Battery voltage im mV / End of charge voltage mV / Soc in %; / Internal Temperature; / External Temperature; / PWM (max 7812) / minutes since reset / CR / LF
0x21 = !		CXN50 sends Adr 0x1000-13ff to PC seperated by ';' / Used tor read out Datalogger starting at Adr 0x0080

Multi Byte Commands
Example: Set Boost voltage to 14400 mV(0x3840
1. Enable eeprom programming for 5 sec
2. Send Boost voltage 3840
ASCII	&GAA0500&M2B3840
HEX	26 47 41 41 30 35 30 30 26 4D 32 42 33 38 34 30

	Comma / n / d	Val1 / 1 Hex-byte= 2 ASCII	Val2 / 1 Hex Byte= / 2 ASCII	Val3 / 1 Hex-byte= 2 ASCII	Default
&	G	AA	Time	xx		Programming of EEPROM enabled for x sec / necessary for all H-Commands
						H-Commands: programming of EEPROM always send first G-Command to enable EEPROM programming
&	H	07	Data MSB	LSB	11000	DC-LOAD:LVD Voltage Voltage dependent
&	H	19	Data MSB	LSB	11000	AC-LAOD:LVD Voltage Voltage dependent
&	H	1B	Data	xx		Lvdmode
&	H	1C	Data	xx		Battery Type
&	H	1D	Data	xx	30(1E)	Daily Boost Time in minutes
&	H	1E	Data	xx	120(78)	Boost Time in minutes
&	H	1F	Data	xx	30(1E)	Max. Days between Equalizations
&	H	20	Data		24	Charge voltage Temperature compensation x * 1 mV
&	H	38	Data	xx	0	Invertersize 1 = 50W
&	H	39	Data	xx		State / 1 = locksettings / 2 = buzzeractive
&	I	ADR / HIGH BYTE	ADR LOW / BYTE	xx		Read data out of ADR up to ADR+16 / RAM: 0x0000 – 0x07ff / EEPROM: 0x1000 – 0x13ff / Option: 0x4800 -0x48FF / TS_V90: 0x4911 / example : &I101000 read address 0x1010-0x101F / Items separated by ';'
&	J	ADR	DATA	xx		Write data to eeprom address (0×1070- 0×10FF) only possible after G-Command / example: &J753700 write to address 0x1075 data 0x37
&	K	55	00	xx		Switch off Load &K5500 (USB)
&	K	55	01	xx		Switch on Load &K5501 (USB)
&	K	55	02	xx		Switch off Inverter
&	K	55	03	xx		Switch on Inverter
&	K	AA	00	xx		Activate Night check
&	K	AB	Data	xx		Activate Keytest for Final Test
&	K	AC	Data	xx		Send Keytest result to PC
&	K	AD	00	xx		Clear AH Counter,datalogger
&	L	DD	00	xx		Load Default and Reset after G-Command
&	L	DD	01	xx		Reset after program enable(&G)
						M-Commands: programming of EEPROM always send first G-Command to enable EEPROM programming
&	M	05	Data MSB	LSB	11900	DC-LOAD:Noload voltage current dependent mv
&	M	17	Data MSB	LSB	11900	AC-LOAD: Noload voltage current dependent mv
&	M	21	Data MSB	LSB	8000	Nightlevel in mv
&	M	23	Data MSB	LSB		Dimming
&	M	25	Data MSB	LSB	15500	Overvoltage mv
&	M	27	Data MSB	LSB	15000	Max. charge voltage mv
&	M	29	Data MSB	LSB	14800	Equalize Voltage mv
&	M	2B	Data MSB	LSB	14400	Boost Voltage mv
&	M	2D	Data MSB	LSB	14200	Min. Boost-voltage mv
&	M	2F	Data MSB	LSB	13800	Float Voltage mv
&	M	31	Data MSB	LSB	13000	Min Charge Voltage = mv
&	M	33	Data MSB	LSB	12800	Reconnect Voltage mv
&	M	35	Data MSB	LSB	10500	Under Voltage mv
&	M	37	Data MSB	LSB	12300	Boost Activation Voltage mv
&	M	39	Data MSB	LSB	12100	Equalize Activation Voltage mv

&	T	00	Year	Month		Send year and month binary to CXN50 / 2015 January : T000F01
&	T	01	Date	Hours		Send day and Hours binary to CXN50 / T01190F 25th day of month 15:00
&	T	02	Minutes	Seconds		Send Minutes and seconds to CXN50 and set time and date.
&	T	03	Xx	Xx		CXN50 sends to PC: / Byte 1: Year / Byte 2: Month / Byte 3: Day / Byte 4: Hours / Byte 5: Minutes / Byte 6: Seconds

						Calibration Command
&	X	Temperature	01	xx		Start Calibration 18000mV with Temperature / CXN50 sends Calibration bytes
&	X	02	02			CXN50 sends Calibration bytes / Byte 1,2: ichargezero MSB first / Byte 3,4: iloadzero MSB first / Byte 5: Calibration Temperature / Byte 6,7: digits for full current load (MSB first) / Byte 8,9:digits for full current charge (MSB first) / Byte 10,11:digits for 18V (MSB first) / Byte 12,13: digits for Temperature / Byte 14,15 :digits for minussense / Byte 16,17 :digits for plussensezer / Byte 17,18 :digits for iextzero(not done yet) / Byte 19,20 :digits for modul zero
&	X	03	03			Write calibration data to EEPROM / Display Calibration okay(Led Soc high on)
&	X	04	04			Leave Calibration mode
&	X	05	05			Display Calibration not okay(red led on)

Description of limit file
0400;	Calibartion : Ichargezero min
0600;	Calibartion : Ichargezero max
0400;	Calibartion : Iloadzero min
0600;	Calibartion : Iloadzero max
5000;	Calibartion : Voltagedigits min for 18V
6000;	Calibartion : Voltagedigits max for 18V
0800;	Calibartion : Digits for full load current min
1000;	Calibartion : Digits for full load current max
0800;	Calibartion : Digits for full charge current min
1000;	Calibartion : Digits for full charge current max
1000;	Calibartion : Temperature ad value min
1400;	Calibartion : Temperature ad value max
49800;	Final test: Voltage min
50200;	Final test: Voltage max
14500;	Final test: Load current min not used
15500;	Final test: Load current max not used
14500;	Final test: Charge current min
15500;	Final test: Charge current max
0001;	Final test: Revision number
0001;	Final test: Manufacturer
0019;	Final test: Device ID
20000;	Max. Cuurent in mA
0255;	Not used Case factors : Case(tempproz)
0255;	Not used Case factors : Fetproz
0255;	Not used Case factors : Cool(cold)
0255;	Not used Case factors : rail
0255;	Not used Case factors : Pwm
0255;	Not used Case factors : load
5010	Sensepluszeromin
5130	Sensepluszeromax
5000	Senseminus Digits min
6000	Senseminus Digits max
3950	Panel zero min
4040	Panel zero max
0000;	Firmware Version
0000;	Gel = 0 ; Flooded = 1
0000;	0 = SOC 1 = LVD
0000;	Max. temperature difference external to internal